## Slide 1
Force Vectors
© 2012 Project Lead The Way, Inc.
Principles of Engineering

## Slide 2: Vectors
Have both a magnitude and direction
Examples: Position, force, moment
Vector Quantities
Vector Notation
Handwritten notation usually includes an arrow, such as
Vectors are given a variable, such as A or B

## Slide 3: Illustrating Vectors
Vectors are represented by arrows
Include magnitude, direction, and sense
30°
+X
Magnitude: The length of the line segment
Magnitude =
3
Notes: Note that the magnitude is the length of the hypotenuse.

## Slide 4: Illustrating Vectors
Vectors are represented by arrows
Include magnitude, direction, and sense
30°
+x
Direction: The angle between a reference axis and the arrow’s line of action
Direction =
30° counterclockwise from the positive x-axis
Notes: Where possible we take the angle from the positive x axis.
1st quadrant

## Slide 5: Illustrating Vectors
Vectors are represented by arrows
Include magnitude, direction, and sense
30°
+x
Sense: Indicated by the direction of the tip of the arrow
Sense =
Upward and to the right

## Slide 6: Sense
+x (right)
+x (right)
-x (left)
-x (left)
+y (up)
+y (up)
-y (down)
-y (down)
(0,0)
Notes: When there is more than one vector force and they are added together, it is crucial to keep track of sense. The standard convention is that right in the X direction is a positive number, and X in the left direction is considered negative. Y in the up direction is positive, and Y in the down direction is negative.

## Slide 7: Trigonometry Review
Hypotenuse (hyp)
90°
Opposite Side (opp)
Adjacent Side (adj)
Right Triangle
A triangle with a 90° angle
Sum of all interior angles = 180°
Pythagorean Theorem: c2 = a2 + b2

## Slide 8: Trigonometry Review
sin θ° = opp / hyp
cos θ° = adj / hyp
tan θ° = opp / adj
Hypotenuse (hyp)
90°
Opposite Side (opp)
Adjacent Side (adj)
Trigonometric Functions soh cah toa

## Slide 9: Trigonometry Application
The hypotenuse is the Magnitude of the Force, F
In the figure here,
The adjacent side is the x-component, Fx
The opposite side is the y-component, Fy
Hypotenuse F
90°
Opposite Side Fy
Adjacent Side Fx
Notes: Note that if the other acute angle had been given, the x-component would be the opposite side!

## Slide 10: Trigonometry Application
sin θ° = Fy / F
cos θ° = Fx / F
tan θ° = Fy / Fx
Hypotenuse F
90°
Opposite Side Fy
Adjacent Side Fx
Fy= F sin θ°
Fx= F cos θ°
Fx and Fy are negative if left or down, respectively.
Notes: This is only true when the angle is measured to the horizontal axis as shown in the picture.

## Slide 11: Vector X and Y Components
35.0°
Vector
Magnitude = 75.0 lb
Direction = 35.0°CCW from positive x-axis
Sense = right, up
+x
+y
-x
-y
Notes: When the x and y components are calculated, it can be assumed that the x component will have a higher value because the vector is closer to the horizontal than the vertical.

## Slide 12: Vector X and Y Components
Solve for
35.0°
+x
+y
-y
-x

## Slide 13: Vector X and Y Components
Solve for
35.0°
+x
+y
-x
-y

## Slide 14: Vector X and Y Components – Your Turn
35.0°
Vector
Magnitude =
Direction =
Sense =
+x
+y
-y
-x
75.0 lb
35.0°CW from positive x-axis
right, down

## Slide 15: Vector X and Y Components – Your Turn
Solve for
35.0°
+x
+y
-y
-x

## Slide 16: Vector X and Y Components – Your Turn
35.0°
+x
+y
-y
-x
Solve for
Notes: The negative is chosen in the second equation because the y-component is in the negative direction. That makes F_By negative, and right triangle trig (SOH-CAH-TOA) assumes positive side lengths.

## Slide 17: Resultant Force
Two people are pulling a boat to shore. They are pulling with the same magnitude.
Notes: This is an example of pulling a boat onto shore.

## Slide 18: Resultant Force
List the forces according to sense.
Label right and up forces as positive, and label left and down forces as negative.
Notes: This slide represents two free body diagrams. The first is a free body diagram with the vector forces shown with their true angles. The second free body diagram shows the vector forces broken into their X and Y components, which is more useful for summing forces.

## Slide 19: Resultant Force
Sum (S) the forces
Magnitude is 122.9 lb
Direction is 0° from the positive x-axis
Sense is right

## Slide 20: Resultant Force
Draw the resultant force ()
Magnitude is 123 lb
Direction is 0° from the positive x-axis
Sense is right

## Slide 21: Resultant Force
Determine the sense, magnitude, and direction for the resultant force.
Notes: Note that the decimal points in the 300. and 400. lb quantities indicate that they have been measured to the nearest 1 lb, not to the nearest 100 lb. This determines how precisely we can know the results of calculations. Keeping track of this precision requires knowledge of “significant figures,” which is beyond the scope of PoE. PoE course materials will use the correct precision in results, the national PoE exam does not require you to know how to handle significant figures.

## Slide 22: Resultant Force
Find the x and y components of vector C.

## Slide 23: Resultant Force
Find the x and y components of vector D.
Notes: When solving for the y-component, the negative is chosen because the y-component for vector D is in the negative direction.

## Slide 24: Resultant Force
List the forces according to sense.
Label right and up forces as positive, and label left and down forces as negative.

## Slide 25: Resultant Force
Sum (S) the forces
Sense is right and up.

## Slide 26: Resultant Force
Draw the x and y components of the resultant force.
496.4 lb
59.8 lb
496.4 lb
59.8 lb
Two equivalent ways to draw the X and Y components
Notes: In order to portray the correct direction for the resultant force, it is crucial that the tail for the first force is the beginning point for the tail of the resultant vector.

## Slide 27: Resultant Force
Solve for magnitude.
496.4 lb
59.8 lb
Magnitude is 500. lb
Notes: The answer has a decimal point shown to indicate it is known to the nearest 1 pound.

## Slide 28
Solve for direction.
496.4 lb
59.8 lb
500. lb
Direction is 7° counterclockwise from the positive x-axis.
Resultant Force

## Slide 29: Resultant Force
Draw the resultant force (FR)
Magnitude = 500. lb
Direction = 7° CCW from positive x-axis
Sense = right and up
7°
500. lb