## Slide 1
Moments
Principles of Engineering

## Slide 2: Moment
The moment of a force is a measure of the tendency of the force to rotate the body upon which it acts.
FORCE
Notes: The force applied to drive the bolt produces a measurable moment, and the wrench rotates about the axis of the bolt.

## Slide 3: Terminology
FORCE
= F
pivot
distance
= d
lever arm
The distance must be perpendicular to the force.

## Slide 4: Moments Formula
FORCE
= F
pivot
Moment
M
M = d x F
distance
= d

## Slide 5: Units for Moments
 | Force | Distance | Moment
English Customary | Pound force (lbf) | Foot (ft) | lbf-ft
SI | Newton (N) | Meter (m) | N-m

## Slide 6: Rotation Direction
In order to add moments, it is important to know if the direction is clockwise (CW) or counterclockwise (CCW).
CCW is positive
CW is negative

## Slide 7: Right-Hand Rule
Curl your fingers to match the direction of rotation.
Thumb is pointing . . . .
Up = Positive
Down = Negative
Toward You = Positive
Away from You = Negative
counterclockwise
+

## Slide 8: Right-Hand Rule
FORCE
THUMB POINTS TOWARD YOU
POSITIVE

## Slide 9: Right-Hand Rule
FORCE
THUMB POINTS AWAY FROM YOU
NEGATIVE

## Slide 10: Moment Calculations
FORCE
F = 20. lb
d = 9.0 in.
M = d x F
Use the right-hand rule to determine positive and negative.
d = 9.0 in. = .75 ft
M = -(20. lb x .75 ft)
M = -15 lb-ft
(15 lb-ft clockwise)
¯
Wrench
Notes: Keep in mind that we have converted to feet to do the calculations.

## Slide 11: Moment Calculations
FORCE
F = 20. lb
d = 1.0 ft
M = d x F
M = -(20. lb x 1.0 ft)
M = -20. lb-ft
¯
Longer Wrench
Notes: If you have a force in the y you are looking for a distance in the x.

## Slide 12: Moment Calculations
FORCE
F = 20. lb
d = 3 in. = .25 ft
M = d x F
M = -(20. lb x .25 ft)
M = -5 lb-ft
¯
3 in.
d = 1.0 ft
L-Shaped Wrench
Notes: If you have a vertical force, you are looking for a horizontal distance to the pivot.
If you have a horizontal force, you are looking for a vertical distance to the pivot.

## Slide 13: Moment Calculations
FORCE
F = 20. lb
d = 8 in. + 10 in. = 1.5 ft
M = d x F
M = -(20. lb x 1.5 ft)
M = -30. lb-ft
¯
8 in.
9 in.
10. in.
Z - Shaped Wrench
Notes: Given a vertical force, look for a horizontal distance.

## Slide 14: Moment Calculations
d = r = 50. cm = 0.50 m
M = d x F
Use the right-hand rule to determine positive and negative.
M = 100 N x 0.50 m
M = 50 N-m
F = 100 N
r = 50. cm
+
Wheel and Axle
Notes: Given a vertical force, look for a horizontal distance.
Since we are in Newtons, convert to meters.

## Slide 15: Moment Calculations
50.o
50.o
Fy = Fsin50.° = (100. N)(.766)
Fy = 76.6N
d = r = 50. cm = 0.50 m
M = d x Fy
M = 76.6 N x 0.50 m
M = 38 N-m
F = 100. N
r = 50. cm
Fy
Wheel and Axle
Notes: Given a vertical force, look for a horizontal distance.
Vector now:
We don’t care about what is going on with the force in the x direction because the distance is zero
If the force is in the x, then we are looking for a distance in the y and there is no distance in the y.

## Slide 16
The state of a body or physical system with an unchanging rotational motion.
  Two cases for that condition:
    Object is not rotating OR
    Object is spinning at a constant speed
  In either case rotation forces are balanced: The sum of all moments about any point or axis is zero.
ΣM = 0
M1 + M2 + M3 . . . = 0
What is Equilibrium?
Notes: Moments
Principles of EngineeringTM
Unit 4 – Lesson 4.1 - Statics
During PoE we will address the first case. We will not have trusses spinning. Trusses will be stationary.

## Slide 17: Moment Calculations
See-Saw

## Slide 18: Moment Calculations
ΣM = 0
M1 + M2 = 0
Use the right-hand rule to determine positive and negative.
M1 = -M2
d1 x F1 = d2 x F2
25lb x 4.0ft - 40. lb x d2=0
100 lb-ft = 40. lb x d2
See-Saw
F1 = 25 lb
F2 = 40. lb
d1 = 4.0 ft
d2 = ? ft
40. lb 40. lb
2.5 ft = d2
+
¯

## Slide 19: Moment Calculations
ΣM = 0
MB + MC = 0
MB = -MC
dAB x RBy = dAC x FC
10.00 ft x RBy = 3.00 ft x 35.0 lb
10.0 ft x RBy = 105 lb-ft
dAB = 10.00 ft
dAC= 3.00 ft
A
C
B
RAy
FC = 35.0 lb
RBy
10.00 ft 10.00 ft
RBy = 10.5 lb
RAy + RBy = 35.0 lb
RAy = 35.0 lb – 10.5 lb = 24.5 lb
Select A as the pivot location. Solve for RBy
Loaded beam

## Slide 20: Moment Calculations
A
B
C
D
Fc = 600. lb
24 ft
8 ft
12 ft
FB = 500. lb
Replace the pinned and roller supports with reaction forces.
RAy
RAx
RDy
Truss
dAC = 24 ft
dCD = 8 ft
dCB = 12 ft
dAD = 32 ft
Notes: This is better said in the truss section, so we skip it.

## Slide 21: Moment Calculations
A
B
C
D
Fc = 600. lb
dAC = 24 ft
dCD = 8 ft
dCB = 12 ft
dAD = 32 ft
24 ft
8 ft
12 ft
FB = 500. lb
RAy
RAx
RDy
Select A as the axis of rotation. Solve for RDY
12 ft
ΣM = 0
MD – MB – MC = 0
MD = MB + MC
dAD x RDy = (dCB x FB) + (dAC x FC)
32 ft x RDy = (12 ft x 500. lb) + (24 ft x 600. lb)
RDy x 32 ft = 6000 lb-ft + 14400 lb-ft
RDy x 32 ft = 20400 lb-ft
32 ft 32 ft
RDY = 640 lb
Truss